## Slide 1: Log Parsing and Graph Plot
Deepakkumar Gupta
  Engineer
@qualcomm
Date: 3/7/2019
Location: Hyderabad

## Slide 2: Procedure:
            Copy log parsing scripts from location:
            \\deegup-linux\workspace\Parse_camx_log (or)
            \\minnie\UMD\CamX\Parse_camx_log
            Use below camx override settings while capturing log for parsing.
            For AEC:
            adb shell “echo logVerboseMask=0x2000000 >> /vendor/etc/camera/camxoverridesettings.txt”
            For AWB:
            adb shell “echo logInfoMask=0x4000000 >> /vendor/etc/camera/camxoverridesettings.txt”

## Slide 3: Procedure:
            The following similar line should be present in log file:
            For AEC:
            [ VERB][STATS_AEC] camxcaecstatsprocessor.cpp:2826 ReadHALAECParam() ReqId:100,
            [ VERB][STATS_AEC] caeccore.cpp:1468: printFrameControl CID:1 FID:2 Mode:PerFrame
            For AWB:
            [ INFO][STATS_AWB] camxcawbioutil.cpp:2311 PublishFrameControlToMainMetadata() Published PropertyIDAWBFrameControl for reqID: 10

## Slide 4: Procedure:
            To run AEC log parser, follow below steps
            Step1: python ParseLog.py <File name or file path>
            Step2: Then choose any one option to plot the graph.

## Slide 5: Procedure:
            Step3: Enter camera ID (0,1,…, etc. or -1 to show graph for all the available camera ids)
            Step4: If you want to plot more graphs then enter 1 else enter 0.

## Slide 6: Procedure:
            To run AWB log parser, follow below steps
            Step1: python ParseLog.py <File name or file path>
            Step2: Enter camera ID (0,1,…, etc. or -1 to show graph for all the available camera ids)
            Step3: If you want to plot more graphs then enter 1 else enter 0.

## Slide 7: Note:
            In case the log file does not have required lines then it will display error message.
            In the below snapshot, I passed log but it does not have any AWB logs.
            If file name not passed into argument then it will display error message.

## Slide 8: Graph:
AEC: Preview

## Slide 9: Graph:
AEC: Flash snapshot

## Slide 10: Graph:
AEC: EV vs Gain & Exposure Time & Sensitivity

## Slide 11: Graph:
AEC: Metering mode vs Gain & Exposure Time

## Slide 12: Graph:
AEC: Anti-banding vs Gain & Exposure time

## Slide 13: Graph:
AEC: Preview with multiple cameras

## Slide 14: Graph:
AEC: Preview with camera ID 0

## Slide 15: Graph:
AEC: Preview with camera ID 1

## Slide 16: Graph:
AWB: Preview

## Slide 17: Graph:
AWB: Flash Snapshot

## Slide 18: Graph:
AWB: Preview with multiple cameras

## Slide 19: Graph:
AWB: Preview with camera ID 0

## Slide 20: Graph:
AWB: Preview with camera ID 1